## Slide 1
5-Level HANPC Rectifier
Semiconductor Losses Calculation
SEEEDS in ZJU
Power Electronics Research Institute
College of Electrical Engineering
Zhejiang University
Email: zyf1125@zju.edu.cn
Weekly Update

## Slide 2
Passive component calculation
1
2
5L Semiconductor Losses
3L Semiconductor Losses
3
CHB Semiconductor Losses
4

## Slide 3
1 Passive component calculation
Minimum inductance usage at different switching frequencies(half of equivalent output frequency), meeting 5% current THD
For this system, when the switching frequency is less than 1.5 kHz, the increase of the switching frequency can reduce the inductance more significantly.

## Slide 4
1 Passive component calculation
LCL-Filter Design
The sum of Inductance is decreased

## Slide 5
1 Passive component calculation
DC Capacitor Design
In order to satisfy the ±5% fluctuation of DC voltage in NPC topology, the capacitor need to be 0.32mF

## Slide 6
1 Passive component calculation
Floating Capacitor Design
When Satisfying the maximum fluctuation on the floating capacitor, the relationship between the switching frequency and the capacitance is shown above.

## Slide 7
Calculation Method
2 Semiconductor Losses
Calculate the parameter of the system, considering the different inductance under different frequency.
Calculate the current ripple in 3-phase system.
Calculate each switch’s conduction losses of IGBT and diode and switching losses.
电压等级 /V | 型号 | 厂商 | 每个开关芯片串联数量 | 每个 IGBT承压 /V | 25℃总串联压降(200A) / V | 25℃单个开关总开关损耗 / mJ | 器件数量 | 载波频率 /Hz | 等效输出频率 /Hz
3300V IGBT | FF200R33KF2C | Infineon | 2 | 1875 | 7.4 | 355.5 | 4×6(switches) ×3(phase) | 450 | 900
1700V IGBT | FF225R17ME4_B11 | Infineon | 4 | 1071.4 | 6.8 | 937.5 | 7×6(switches) ×3(phase) | 900 | 1800
1700V SiC | CAS300M17BM2 | Cree | 4 | 1071.4 | 5.69 | 85.19 | 7×6(switches) ×3(phase) | 3600 | 3600
1200V SiC | CAS300M12BM2 | Cree | 5 | 750 | 2.8 | 49.58 | 10×6(switches) ×3(phase) | 7200 | 7200

## Slide 8
Losses under different load
2 Semiconductor Losses
Chart: Efficiency at Differnt Load under certain frequency
| 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
1700V IGBT at 900Hz Switching Frequency | 0.99191 | 0.99244 | 0.99254 | 0.99256 | 0.99247 | 0.99229
3300V IGBT at 450Hz Switching Frenquency | 0.99728 | 0.99741 | 0.9974 | 0.99734 | 0.99719 | 0.99703
At this Frequency, the most efficiency point is around 1.2MW

## Slide 9
Losses under different frequency
2 Semiconductor Losses
Chart: 1700V IGBT Losses under different frequency
| 450 | 600 | 750 | 900 | 1050 | 1200 | 1350 | 1500 | 1650 | 1800 | 1950 | 2100 | 2250 | 2400 | 2550 | 2700 | 2850 | 3000 | 3150 | 3300 | 3450 | 3600 | 3750 | 3900 | 4050 | 4200 | 4350 | 4500 | 4650 | 4800 | 4950
Conduction Losses | 4323.0413 | 4323.4411 | 4323.1 | 4323.3718 | 4323.2619 | 4323.2487 | 4323.2517 | 4323.3322 | 4323.2414 | 4323.289 | 4323.2616 | 4323.2494 | 4323.2431 | 4323.2919 | 4323.2537 | 4323.2712 | 4323.2764 | 4323.2732 | 4323.2539 | 4323.2523 | 4323.2704 | 4323.2824 | 4323.2743 | 4323.2564 | 4323.2631 | 4323.27 | 4323.2472 | 4323.2836 | 4323.2501 | 4323.2553 | 4323.2661
Switching Losses | 534.1315 | 716.5091 | 891.4388 | 1069.7992 | 1245.015 | 1423.1009 | 1599.9586 | 1777.1049 | 1953.7869 | 2130.5109 | 2306.9927 | 2484.5664 | 2661.283 | 2838.204 | 3014.601 | 3192.13 | 3369.8367 | 3545.9602 | 3722.5838 | 3899.8873 | 4076.4366 | 4253.8817 | 4430.9614 | 4607.6615 | 4784.4482 | 4961.7084 | 5138.6805 | 5315.5096 | 5492.1235 | 5669.6003 | 5846.3413
Chart: 3300V IGBT Losses under different frequency
| 450 | 600 | 750 | 900 | 1050 | 1200 | 1350 | 1500 | 1650 | 1800 | 1950 | 2100 | 2250 | 2400 | 2550 | 2700 | 2850 | 3000 | 3150 | 3300 | 3450 | 3600 | 3750 | 3900 | 4050 | 4200 | 4350 | 4500 | 4650 | 4800 | 4950
Conduction Losses | 3924.775 | 3925.2706 | 3924.767 | 3925.0952 | 3924.9445 | 3925.0734 | 3924.9253 | 3925.0593 | 3924.9825 | 3925.095 | 3925.0287 | 3925.0633 | 3924.9946 | 3925.0908 | 3925.0441 | 3925.0678 | 3925.0769 | 3925.0975 | 3925.0499 | 3925.0277 | 3925.0723 | 3925.1136 | 3925.0785 | 3925.0573 | 3925.0722 | 3925.0764 | 3925.0298 | 3925.1196 | 3925.0349 | 3925.0622 | 3925.0756
Switching Losses | 1536.7307 | 2059.0238 | 2561.066 | 3073.3192 | 3574.4987 | 4086.4621 | 4599.2496 | 5101.9037 | 5602.9723 | 6113.4507 | 6617.2247 | 7128.3907 | 7640.4368 | 8141.8503 | 8644.9743 | 9155.0418 | 9662.0319 | 10168.1362 | 10673.7185 | 11181.802 | 11689.3635 | 12196.1349 | 12704.071 | 13209.4662 | 13715.4849 | 14222.4549 | 14727.5544 | 15235.975 | 15741.7607 | 16249.7464 | 16759.0733

## Slide 10
Losses under different frequency
2 Semiconductor Losses
Chart: 1700V SiC Losses under different frequency
| 450 | 600 | 750 | 900 | 1050 | 1200 | 1350 | 1500 | 1650 | 1800 | 1950 | 2100 | 2250 | 2400 | 2550 | 2700 | 2850 | 3000 | 3150 | 3300 | 3450 | 3600 | 3750 | 3900 | 4050 | 4200 | 4350 | 4500 | 4650 | 4800 | 4950
Conduction Losses | 2799.0215 | 2799.0215 | 2799.0214 | 2799.0214 | 2799.0214 | 2799.0214 | 2799.0214 | 2799.0214 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213 | 2799.0213
Switching Losses | 55.4531 | 75.9062 | 95.0309 | 114.7585 | 134.0557 | 153.6005 | 172.9228 | 192.4428 | 211.7822 | 231.2809 | 250.6373 | 270.1121 | 289.4532 | 308.9452 | 328.3234 | 347.7596 | 367.1554 | 386.5905 | 405.964 | 425.4068 | 444.8107 | 464.2463 | 483.6484 | 503.0667 | 522.4618 | 541.8934 | 561.2934 | 580.7138 | 600.1175 | 619.5377 | 638.9199
Chart: 1200V SiC Losses under different frequency
| 450 | 600 | 750 | 900 | 1050 | 1200 | 1350 | 1500 | 1650 | 1800 | 1950 | 2100 | 2250 | 2400 | 2550 | 2700 | 2850 | 3000 | 3150 | 3300 | 3450 | 3600 | 3750 | 3900 | 4050 | 4200 | 4350 | 4500 | 4650 | 4800 | 4950
Conduction Losses | 2234.4867 | 2234.4867 | 2234.4867 | 2234.4866 | 2234.4866 | 2234.4866 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865 | 2234.4865
Switching Losses | 51.9307 | 69.8128 | 87.106 | 104.6467 | 121.9948 | 139.453 | 156.8094 | 174.2331 | 191.5778 | 209.0177 | 226.3796 | 243.8006 | 261.1701 | 278.5707 | 295.9348 | 313.3386 | 330.7268 | 348.1116 | 365.5007 | 382.8777 | 400.2555 | 417.6534 | 435.0422 | 452.4231 | 469.8002 | 487.1905 | 504.5696 | 521.9569 | 539.3305 | 556.7251 | 574.1015

## Slide 11
Losses under different frequency
2 Semiconductor Losses
 | FF225R17ME4_B11 | FF200R33KF2C
Inductance/mH | 0.008297 | 0.016934
Switching frequency/Hz | 1800 | 900
IGBT Conduction Loss(W) | 4323.289 | 3925.095
IGBT switching loss(W) | 2130.511 | 3073.319
Rec total loss(W) | 6453.8 | 6998.414
Rec Semi Efficiency(%) | 0.990319 | 0.989502
 | CAS300M17BM2 | CAS300M12BM2
Inductance/mH | 0.008297 | 0.016934
Switching frequency/Hz | 3600 | 3600
IGBT Conduction Loss(W) | 2799.02133 | 2234.4865
IGBT switching loss(W) | 464.246276 | 417.653417
Rec total loss(W) | 3263.26761 | 2652.13992
Rec Semi Efficiency(%) | 0.9951051 | 0.99602179
Under the same switching frequency, the 1200V SiC is more efficiency than 1700V SiC ,because of the lower conduction losses and switching losses.
SiC MOS is better than Si IGBT，

## Slide 12
Losses under different frequency
2 Semiconductor Losses
The higher frequency the lower efficiency and the lower inductance, mainly because of the switching losses.
The conduction losses of 3300V IGBT is lower than that of 1700V IGBT, but the switching losses is much higher.so that, the 1700V IGBT is prefer.
Chart: Efficiency Comparison
| 450 | 600 | 750 | 900 | 1050 | 1200 | 1350 | 1500 | 1650 | 1800 | 1950 | 2100 | 2250 | 2400 | 2550 | 2700 | 2850 | 3000 | 3150 | 3300 | 3450 | 3600 | 3750 | 3900 | 4050 | 4200 | 4350 | 4500 | 4650 | 4800 | 4950
1700V IGBT Efficiency | 0.99271 | 0.99244 | 0.99218 | 0.99191 | 0.99165 | 0.99138 | 0.99112 | 0.99085 | 0.99058 | 0.99032 | 0.99005 | 0.98979 | 0.98952 | 0.98926 | 0.98899 | 0.98873 | 0.98846 | 0.9882 | 0.98793 | 0.98767 | 0.9874 | 0.98713 | 0.98687 | 0.9866 | 0.98634 | 0.98607 | 0.98581 | 0.98554 | 0.98528 | 0.98501 | 0.98475
3300V IGBT efficiency | 0.99181 | 0.99102 | 0.99027 | 0.9895 | 0.98875 | 0.98798 | 0.98721 | 0.98646 | 0.98571 | 0.98494 | 0.98419 | 0.98342 | 0.98265 | 0.9819 | 0.98114 | 0.98038 | 0.97962 | 0.97886 | 0.9781 | 0.97734 | 0.97658 | 0.97582 | 0.97506 | 0.9743 | 0.97354 | 0.97278 | 0.97202 | 0.97126 | 0.9705 | 0.96974 | 0.96897
1700V SiC efficiency | 0.99572 | 0.99569 | 0.99566 | 0.99563 | 0.9956 | 0.99557 | 0.99554 | 0.99551 | 0.99548 | 0.99545 | 0.99543 | 0.9954 | 0.99537 | 0.99534 | 0.99531 | 0.99528 | 0.99525 | 0.99522 | 0.99519 | 0.99516 | 0.99513 | 0.99511 | 0.99508 | 0.99505 | 0.99502 | 0.99499 | 0.99496 | 0.99493 | 0.9949 | 0.99487 | 0.99484
1200V SiC efficiency | 0.99657 | 0.99654 | 0.99652 | 0.99649 | 0.99647 | 0.99644 | 0.99641 | 0.99639 | 0.99636 | 0.99633 | 0.99631 | 0.99628 | 0.99626 | 0.99623 | 0.9962 | 0.99618 | 0.99615 | 0.99613 | 0.9961 | 0.99607 | 0.99605 | 0.99602 | 0.996 | 0.99597 | 0.99594 | 0.99592 | 0.99589 | 0.99587 | 0.99584 | 0.99581 | 0.99579

## Slide 13
1700V IGBT Losses
2 Semiconductor Losses
The higher frequency the lower efficiency, mainly because of the switching losses.
At high frequency, the lighter load the lower efficiency.
Chart: Effiency at Different Load Under Certain Frequency
| 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
600Hz | 0.99591 | 0.99624 | 0.99632 | 0.99637 | 0.99638 | 0.99633
1800Hz | 0.9947 | 0.9948 | 0.99476 | 0.99463 | 0.99434 | 0.99405
3000Hz | 0.99349 | 0.99335 | 0.9932 | 0.99288 | 0.9923 | 0.99176
4200Hz | 0.99227 | 0.99191 | 0.99164 | 0.99114 | 0.99026 | 0.98948
5400Hz | 0.99106 | 0.99046 | 0.99007 | 0.98939 | 0.98822 | 0.98719
6600Hz | 0.98985 | 0.98901 | 0.98851 | 0.98765 | 0.98618 | 0.9849
7800Hz | 0.98863 | 0.98757 | 0.98695 | 0.9859 | 0.98414 | 0.98262
9000Hz | 0.98742 | 0.98612 | 0.98539 | 0.98416 | 0.9821 | 0.98033
10200Hz | 0.9862 | 0.98467 | 0.98382 | 0.98241 | 0.98006 | 0.97805

## Slide 14
3300V IGBT Losses
2 Semiconductor Losses
The higher frequency the lower efficiency, mainly because of the switching losses.
At high frequency, the lighter load the lower efficiency.
Chart: Effiency at Different Load Under Certain Frequency
| 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
600Hz | 0.99551 | 0.99564 | 0.99557 | 0.9954 | 0.99505 | 0.9947
1800Hz | 0.99247 | 0.99189 | 0.99142 | 0.99064 | 0.98927 | 0.98807
3000Hz | 0.98943 | 0.98814 | 0.98727 | 0.98588 | 0.98349 | 0.98144
4200Hz | 0.98639 | 0.9844 | 0.98313 | 0.98112 | 0.97771 | 0.97481
5400Hz | 0.98335 | 0.98065 | 0.97898 | 0.97636 | 0.97193 | 0.96817
6600Hz | 0.98031 | 0.9769 | 0.97484 | 0.9716 | 0.96615 | 0.96154
7800Hz | 0.97727 | 0.97316 | 0.97069 | 0.96684 | 0.96037 | 0.95491
9000Hz | 0.97423 | 0.96941 | 0.96654 | 0.96208 | 0.95459 | 0.94827
10200Hz | 0.97119 | 0.96566 | 0.9624 | 0.95732 | 0.94881 | 0.94164

## Slide 15
1200V SiC Losses
2 Semiconductor Losses
The higher frequency the lower efficiency, mainly because of the switching losses.
At low frequency, the lighter load the lower efficiency.
Chart: Effiency at Different Load Under Certain Frequency
| 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
450Hz | 0.99829 | 0.99894 | 0.99909 | 0.99924 | 0.99939 | 0.99946
600Hz | 0.99827 | 0.99892 | 0.99907 | 0.99922 | 0.99936 | 0.99943
750Hz | 0.99826 | 0.9989 | 0.99905 | 0.9992 | 0.99934 | 0.9994
900Hz | 0.99825 | 0.99888 | 0.99903 | 0.99917 | 0.99931 | 0.99936
1050Hz | 0.99823 | 0.99887 | 0.99901 | 0.99915 | 0.99928 | 0.99933
1200Hz | 0.99822 | 0.99885 | 0.99899 | 0.99913 | 0.99925 | 0.9993
1350Hz | 0.99821 | 0.99883 | 0.99897 | 0.99911 | 0.99922 | 0.99926
1500Hz | 0.99819 | 0.99882 | 0.99895 | 0.99908 | 0.99919 | 0.99923
1650Hz | 0.99818 | 0.9988 | 0.99894 | 0.99906 | 0.99916 | 0.9992
1800Hz | 0.99817 | 0.99878 | 0.99892 | 0.99904 | 0.99914 | 0.99917
1950Hz | 0.99815 | 0.99876 | 0.9989 | 0.99901 | 0.99911 | 0.99913
2100Hz | 0.99814 | 0.99875 | 0.99888 | 0.99899 | 0.99908 | 0.9991

## Slide 16
1700V IGBT Losses
2 Semiconductor Losses
The higher frequency the lower efficiency, mainly because of the switching losses.
At low frequency, the lighter load the lower efficiency.
Chart: Effiency at Different Load Under Certain Frequency
| 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
600Hz | 0.99769 | 0.99865 | 0.99886 | 0.99906 | 0.99926 | 0.99936
1800Hz | 0.99755 | 0.99851 | 0.99871 | 0.99889 | 0.99908 | 0.99916
3000Hz | 0.99742 | 0.99836 | 0.99855 | 0.99873 | 0.99889 | 0.99897
4200Hz | 0.99729 | 0.99821 | 0.9984 | 0.99856 | 0.99871 | 0.99877
5400Hz | 0.99715 | 0.99806 | 0.99824 | 0.9984 | 0.99853 | 0.99857
6600Hz | 0.99702 | 0.99792 | 0.99809 | 0.99823 | 0.99835 | 0.99838
7800Hz | 0.99689 | 0.99777 | 0.99794 | 0.99807 | 0.99817 | 0.99818
9000Hz | 0.99675 | 0.99762 | 0.99778 | 0.9979 | 0.99798 | 0.99799
10200Hz | 0.99662 | 0.99747 | 0.99763 | 0.99774 | 0.9978 | 0.99779

## Slide 17
3 3-L Semiconductor Losses
电压等级 /V | 型号 | 厂商 | 每个开关芯片串联数量 | 每个 IGBT承压 /V | 25℃总串联压降(200A) / V | 25℃单个开关总开关损耗 / mJ | 器件数量 | 载波频率 /Hz | 等效输出频率 /Hz
3300V IGBT | FF200R33KF2C | Infineon | 4 | 1875 | 12.95 | 711.11 | 4×6(switches) ×3(phase) | 450 | 450
1700V IGBT | FF225R17ME4_B11 | Infineon | 7 | 1071.4 | 13.6 | 1875 | 7×6(switches) ×3(phase) | 900 | 900
1700V SiC | CAS300M17BM2 | Cree | 7 | 1071.4 | 9.96 | 170.37 | 7×6(switches) ×3(phase) | 3600 | 3600
1200V SiC | CAS300M12BM2 | Cree | 10 | 750 | 5.6 | 99.17 | 10×6(switches) ×3(phase) | 7200 | 7200

## Slide 18
4 CHB Semiconductor Losses
System Parameter

## Slide 19
4 CHB Semiconductor Losses
CHB 1700V IGBT
At high frequency, the lighter load the lower efficiency.
At same equivalent output frequency, CHB has a little more conduction losses than 5L-ANPC but much lower switching Losses.
At same switching frequency, compared to 5L-ANPC, although the total losses is large, but higher voltage level and higher output frequency.

## Slide 20
4 CHB Semiconductor Losses
3L+CHB 1700V IGBT
At high frequency, the lighter load the lower efficiency.
Compared to 1700V IGBT CHB, the conduction Losses and switching losses are not much different between the two topology. What’s more it Appear more voltage levels.

## Slide 21
4 CHB Semiconductor Losses
CHB 1200V SiC MOSFET
At high frequency, the lighter load the lower efficiency, at low frequency, the situation is reversed.
At same equivalent output frequency, CHB has a little more conduction losses than 5L-ANPC but much lower switching Losses.At same switching frequency, compared to 5L-ANPC, although the total losses is large, but higher voltage level and higher output frequency.
Compared to all kinds of IGBT, SiC is also prefered in CHB.

## Slide 22
4 CHB Semiconductor Losses
3L+CHB 1200V SiC MOSFET
At high frequency, the lighter load the lower efficiency.
Compared to 1200V SiC CHB, the conduction Losses and switching losses are not much different between the two topology. What’s more it Appear more voltage levels.

## Slide 23
4 CHB Semiconductor Losses
CHB 3300V IGBT
At high frequency, the lighter load the lower efficiency.
At same equivalent output frequency, CHB has a little more conduction losses than 5L-ANPC but much lower switching Losses.
At same switching frequency, compared to 5L-ANPC, although the total losses is large, but higher voltage level and higher output frequency.
Compared to 1700V IGBT, 3300V IGBT has lower conduction losses, but much higher switching losses and total losses which is similar with the situation of ANPC

## Slide 24
5 Final Project
CHB 3-L 1200SiC
LOAD/MW | 2 | 1.2 | 1 | 0.8 | 0.6 | 0.5
EFFICIENCY/% | 0.995516 | 0.995647 | 0.995462 | 0.995077 | 0.994294 | 0.993603
Chart: Total Losses at 10kHz Switching Frequency
| Conduction Losses /W | Switching Losses/W
 | 2919 | 3114

## Slide 25
Thanks
Sustainable & Efficient Electric Energy Delivery Systems Laboratory